## Slide 1: Constellation Classification
Alex Knowlton

## Slide 2: Problem Statement
Digital communications transmit bits using a constellation
  Digital bits mapped to M constellation points
  bits transmitted per symbol
Constellations usually known
Tough to decode otherwise
Channel is noisy
  High SNR – more power in transmitter
  Low SNR – harder to decode
What to do when you don't know the constellation?

## Slide 3: Problem Statement, cont'd
Analytical solution is very intense
  Calculate Euclidean distance of received signal to each constellation point
  Find minimum Euclidean distance
  Lowest average Euclidean distance is most likely constellation
Goal: approximate using a neural network
PAM more likely

## Slide 4: Problem Statement, cont'd
Further problem: fading channels
  Channels are both noisy and lossy
  At a given frequency:
  Received data attenuated, rotated, and noisy

## Slide 5: Methodology
Data is a vector of randomly sampled values from constellation
  Real and complex values, so shape of (512, 2)
  Convolution with a kernel of size (1, 2)
  Output is correlation of convolution with signal
  High correlation means signal likely
Contiguous data points unrelated
  Most likely points = feature selection
  Convolution to calculate similarity
    Output gives correlation with a point in all constellations
    Output most likely kernels to fully-connected network

## Slide 6: Methodology, Channel Modeling
Channel modeled as complex values
  Amplitude and phase shift
  Equivalent to convolution
  Padding with 2 zeros and stride=2
Equivalent to complex multiplication

## Slide 7: Methodology, activity score
If activity score known, it becomes a feature
  Use softmax to calculate kernel activity
  Differentiable, backpropagation possible
Most active convolutions lead to most likely constellation points, allows prediction
Features passed through fully-connected network to predict constellation

## Slide 8: Implementation
Softmax
Conv2D
softmax
(Activity score)
ReLU
ReLU
Softmax

## Slide 9: Evaluation
Simulated dataset
  6 constellations
  5000 training vectors
    SNR various so model sees some noise
    Length = 512 complex values
    Size = (512, 2)
  4 channels (if predicting with channel)
Accuracy score
  All constellations equally likely
  All channels equally likely
Model performed very well with high enough signal-to-noise ratio

## Slide 10: Challenges
Dataset generation
  Real data not feasible, generated instead
  Used an approximation that from EECS598-002
  Generate NxD numpy array and feed that to PyTorch
Differentiable activity score
  Couldn't just use max()
  Softmax worked well
Modeling Channels
  PyTorch model with channel effectively guessing (16% accuracy, 1/6)
  Channel modeling not effective

## Slide 11: Future work
Potential for work in distress signals or surveillance
Channel modeling needs work
Currently supervised learning
  Must know roughly how many constellation points are being used
  Might have application in unsupervised learning
  Teach itself constellations
  K-means might be effective here

## Slide 12: References
[1] Stark, Wayne. Introduction to Digital Communications. 1st ed., Cambridge University Press, 2023.
[2] Shannon, Claude Elwood, and Warren Weaver. The Mathematical Theory of Communication. University of Illinois Press, 1949.
[3] R. R. Selvaraju, M. Cogswell, A. Das, R. Vedantam, D. Parikh and D. Batra, "Grad-CAM: Visual Explanations from Deep Networks via Gradient-Based Localization," 2017 IEEE International Conference on Computer Vision (ICCV), Venice, Italy, 2017, pp. 618-626, doi: 10.1109/ICCV.2017.74.

## Slide 13: Recording Link
https://youtu.be/glsg7tVp5_4